## Slide 1
Live-Cell Kinetic Assays for Monitoring Cell Health and Metabolism
Vojtěch Ledvina, Ph.D.
vojtech.ledvina@eastport.cz

## Slide 2
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Basic modes of detection

## Slide 3
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Basic modes of detection

## Slide 4
Production of light by living organisms
Light produced by enzymatic oxidation of a substrate luciferin by an enzyme luciferase
Common in marine vertebrates and inverebrates, fungi, bacteria
Most used luciferases are – Firefly, Renilla, NanoLuc and Gaussia luciferases
Bioluminescence

## Slide 5
ATP-dependent luciferase
Universal reaction adaptable for various assays
Ultra-GloTM rLuciferase
  Higher stability in the presence of detergent and reducing agents
  More robust signal – less temperature signal variance
Photinus pyralis
Firefly Luciferase

## Slide 6: NanoLuc® Luciferase – Novel Experimental Reporter
Oplophorus gracilirostris
ATP-independent luciferase from a deep sea shrimp
100x brigther than Rluc and Fluc, glow-type luminescence
Smallest luciferase – 19,1 kDa
Complementation reporter
Luciferase expression
NanoBRET assays
Light
Nluc
NanoLuc
luciferase
O2
Notes: Lze kombinovat s coelenterazinem H – nižší signál, autofluorescence
Konkurence Gaussia luciferase

## Slide 8
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Other modes of detection

## Slide 9
Other Modes of Detection

## Slide 10
ABSORBANCE
FLUORESCENCE
LUMINISCENCE
YES
NO!
“clear“
“white”
“solid or clear bottom”
TC treated
Sterile
With lid
Matching Plate Type and Detection Mode
“black”
YES
YES
(YES)
(YES)
„solid or clear bottom“
(YES)
• 400 – 800 nm (VIS)
• 200 – 400 nm (UV)
quarz glass
cyclic olefin copolymer
(COC)
plastic autofluorescence (↓)
background (↓)
crosstalk (↓)
maximal reflection
crosstalk (↓)
(!) phosphorescence

## Slide 11
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Basic modes of detection

## Slide 12
What Defines a Live-Cell Kinetic Assay?
Live-Cell Kinetic Assays…
…are non-toxic & maintain cellular integrity
…allow monitoring a parameter of a sample over extended period of time
…maximize the information gained from one sample within a given time window
…typically allow for extended time course analysis (days)
Endpoint assay
Start
End
Start
End
Kinetic assay

## Slide 13
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Basic modes of detection

## Slide 14
Benefits of Live-Cell Kinetic Assays
Data quantity / reliability
More data per well
Easy identification of important time points
Draw valid conclusions from your experiments
Economical savings/resource efficient
Saves your precious cells, reagents, consumables…
Time-efficient identification of important time points
Draw valid conclusions
Flexibility
Combine with other assays (multiplexing) for enhanced data reliability and interpretation
Usually compatible with both 2D and 3D cell culture models
Compatible with both, time course and endpoint analysis
No additional instrumentation required
Heating function and gas control is beneficial but optional
(Multimode functionality)

## Slide 15: Studying targeted protein degradation with HiBiT
JQ1
Thalidomide = dBET1
Evaluation of Proteolysis targeting chimeras (PROTACs) Efficiency
BRD
4 hours
16 hours
0.0
0.5
1.0
1.5
rel. Luminescence [RLU]
BRD4 BRD3 BRD2
Endpoint
10
0.0
0
0.5
1.0
rel. Luminescence [RLU]
BRD2 BRD3 BRD4
16 20
Time [h]
4
Real-Time
Notes: JQ1 – thienotriazolodiazepine, potent inhibitor of the BET family of bromodomain proteins (BRD2, BRD3, BRD4 and the testis-specific protein BRDT in mammals)
Thalidomide – binds to cereblon (CRBN) which is a part of the ubiquitin E3 ligase, causes ubiquitinylation of the BRD protein and degradation
Thalidomide

## Slide 16
Benefits of Live-Cell Kinetic Assays
Data quantity / reliability
More data per well
Easy identification of important time points
Draw valid conclusions from your experiments
Economical savings/resource efficient
Saves your precious cells, reagents, consumables…
Time-efficient identification of important time points
Flexibility
Combine with other assays (multiplexing) for enhanced data reliability and interpretation
Usually compatible with both 2D and 3D cell culture models
Compatible with both, time course and endpoint analysis
No additional instrumentation required
Heating function and gas control is beneficial but optional
(Multimode functionality)

## Slide 17: CellTox™ Green Cytotoxicity Assay
HepG2
Early Apoptosis
(1 µM)
Determine Membrane Integrity Using a Fluorescent DNA-binding Dye
endpoint
real-time
1
less medium, cells and reagent
VS.
Notes: Staurosporin - ATP-competitive kinase inhibitor with high affinity and low selectivity

## Slide 18
Benefits of Live-Cell Kinetic Assays
Data quantity / reliability
More data per well
Easy identification of important time points
Draw valid conclusions from your experiments
Economical savings/resource efficient
Saves your precious cells, reagents, consumables…
Time-efficient identification of important time points
Flexibility
Combine with other assays (multiplexing) for enhanced data reliability and interpretation
Usually compatible with both 2D and 3D cell culture models
Compatible with both, time course and endpoint analysis
No additional instrumentation required
Heating function and gas control is beneficial but optional
(Multimode functionality)

## Slide 19
Secondary Necrosis
Early Apoptosis
RealTime-Glo® Annexin V Apoptosis and Necrosis Assay
A Live Cell Kinetic Multiplexing Assay per se

## Slide 20
Benefits of Live-Cell Kinetic Assays
Data quantity / reliability
More data per well
Easy identification of important time points
Draw valid conclusions from your experiments
Economical savings/resource efficient
Saves your precious cells, reagents, consumables…
Time-efficient identification of important time points
Flexibility
Combine with other assays (multiplexing) for enhanced data reliability and interpretation
Usually compatible with both 2D and 3D cell culture models
Compatible with both, time course and endpoint analysis
No additional instrumentation required
Heating function and gas control is beneficial but optional
(Multimode functionality)

## Slide 21
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Basic modes of detection

## Slide 22
Edge Effect
Plate layout
Temperature
Evaporation
What to Consider When Using Live-Cell Kinetic Assays?

## Slide 23
Evaporation
384-
96-
1563-
48-
24-
12-
6-well
Worki
0.1 – 0.2 ml
ng Volume
1 – 3 ml
0.5 – 1 ml
5 – 10 µl
Edge Effect Incubation time
The Edge Effect
Experimental Plate Layout and Data Variability
Use specialized plates/seals for culturing of cells
Fill outer 36 wells (and inter-well space)
with pre-equilibrated sterile water or PBS
Avoid shuttling of plates or hurry up
Keep temperature constant over time
Pre-quilibrate to reading temperature

## Slide 24
37°C
CO2
~ 95% humidity
Seal *
Lid
24 hours
Counteracting the Edge Effect
* gas permeable
37°C
Media Evaporation During Extended Incubations

## Slide 25
100 µl/well
24 hours
37°C
n = 4
11
10
11
23
0
10
20
30
40
50
60
+ Seal
+ Lid
Evaporation [%]
Incubator
inner wells outer wells
30
13
29
46
0
10
20
30
40
50
60
+ Seal
+ Lid
Evaporation [%]
Plate-reader
inner wells
outer wells
Conclusions
Plate seals can help to alleviate the edge effect
If one can spare the outer wells, a lid is an
excellent strategy too
Even under non-humidified conditions, a lid ensures a relatively low degree of evaporation in the inner wells
Counteracting the Edge Effect
Media Evaporation During Extended Incubations

## Slide 26
Edge Effect
Plate layout
Temperature
Evaporation
Instrumentation
No CO2 control? → CO2-independent medium
Heating?
Condensation on the lid
Software and protocol setup
What to Consider When Using Live-Cell Kinetic Assays?

## Slide 27
Instrumentation for Kinetic Assays
No additional instrumentation needed
Temperature and CO2 control are beneficial but not required
No CO2 control? → use CO2-independent medium
No heating? → shuttle the plate between the incubator and luminometer
Condensation on the lid?
  Cover the inside of the lid with 1-2 ml of 0,5% Triton X-100 in sterile water or PBS
  Remove the liquid and let dry for a while
  Return the lid on the plate
Heating needs to be activated
Heating step needs to be incorporated in the “Loop”

## Slide 28
Edge Effect
Plate layout
Temperature
Evaporation
Instrumentation
No CO2 control? → CO2-independent medium
Software and protocol setup
Condensation on the lid
Length of measurements
Always check the manual for the actual length of measurement – 24, 48, 72 hours
What to Consider When Using Live-Cell Kinetic Assays?

## Slide 29
Today‘s Agenda
6
Which Live-Cell Kinetic Assay Do We Offer?
5
What to Consider When Using Live-Cell Kinetic Assays?
4
What Are the Benefits of Live-Cell Kinetic Assay?
3
What Defines a Live-Cell Kinetic Assay?
2
Bioluminescence
1
Basic modes of detection

## Slide 30
Which Live-Cell Kinetic Assay Do We Offer?
e.g. Caspase-Glo® CellTiter-Glo®…
e.g. ADP-Glo®
e.g. CellTiter-Blue® CellTiter-96® AQ CellTiter-FluorTM
e.g. LDH-GloTM,
Glucose-GloTM…
e.g. RealTime-GloTM
CellTox-GreenTM…
Assays
Biochemical
Cell-Based
Lytic
Live-Cell
Kinetic
Endpoint
Kinetic
Timed kinetic
Notes: JQ1 – thienotriazolodiazepine, potent inhibitor of the BET family of bromodomain proteins (BRD2, BRD3, BRD4 and the testis-specific protein BRDT in mammals)
Thalidomide – binds to cereblon (CRBN) which is a part of the ubiquitin E3 ligase, causes ubiquitinylation of the BRD protein and degradation
Thalidomide

## Slide 31
Live-Cell Kinetic Assays
Real-Time Kinetic
RealTime-GloTM MT Cell Viability Assay
RealTime-GloTM Annexin V Apoptosis / Necrosis Assay
RealTime-GloTM Extracellular ATP Assay
CellTox-GreenTM Cytotoxicity Assay
Nano-Glo® Live Cell Assay System
Nano-Glo® VivazineTM Live Cell Substrate
Nano-Glo® EndurazineTM Live Cell Substrate
Workflow
Cytotoxicity
Metabolic phenotype
Apoptosis
Cell Viability
Protein:Protein Interactions
Target Engagement
Reporter Expression
Continuous reading from one well
Less hands-on time (no transfer steps required)
Non-toxic for the cells
Number of data points is limited only by instrument/software

## Slide 32
Timed Kinetic Live-Cell Assays
Timed Kinetic
LDH-GloTM Cytotoxicity Assay
Glucose-GloTM Assay
Lactate-GloTM Assay
Glutamate/Glutamine-GloTM Assay
Glutamate-GloTM Assay
Workflow
Cytotoxicity
Metabolic phenotype
Require periodic sampling of supernatant
Higher hands on time (sampling, dillution, transfer, assay…)
High sensitivity
Number of data points is limited by sampling volume/assay sensitivity

## Slide 33
Coffee time!
We will continue at 10:50

## Slide 34
Real Time-Glo MT Cell Viability Assay
True kinetic nonlytic assay based on the NanoLuc luciferase
NanoLuc and prosubstrate pro-furimazine added to the medium
Pro-furimazine diffuses into the cells where it is reduced
Reduced furimazine is released into the medium and processed by the NanoLuc which generates bioluminescence
Suitable for kinetic measurements up to 72 hours

## Slide 35
Real Time-Glo MT Assay – workflow a data
Notes: Bortezomib – blocks the 26S proteasomal subunit and induces apoptosis

## Slide 36
„endpoint“ vs. „real-time“
and much less medium, cells and reagent
Real Time-Glo MT Assay – Workflow and Data

## Slide 37: Furimazine does not accumulate in cells
time [min]
+ 1% Triton x-100

## Slide 38
RealTime-Glo Extracellular ATP Assay
Damage-associated molecular patterns (DAMPs) are molecules released into extracellular space as an indicator of cell damage or infection
eATP can function as one of DAMPs and trigger inflammasome activation
eATP
Notes: JQ1 – thienotriazolodiazepine, potent inhibitor of the BET family of bromodomain proteins (BRD2, BRD3, BRD4 and the testis-specific protein BRDT in mammals)
Thalidomide – binds to cereblon (CRBN) which is a part of the ubiquitin E3 ligase, causes ubiquitinylation of the BRD protein and degradation
Thalidomide

## Slide 39
RealTime-Glo Extracellular ATP Assay
Bioluminescent assay for kinetic monitoring of ATP release from dying, stressed or activated cells
Assay suitable for detecting immunogenic cell death or inflammasome activation
Based on the modified Firefly luciferase
Enzyme and substrate are added to the cells and ATP is supplied from the medium
Compatible with 2D and 3D models
Notes: JQ1 – thienotriazolodiazepine, potent inhibitor of the BET family of bromodomain proteins (BRD2, BRD3, BRD4 and the testis-specific protein BRDT in mammals)
Thalidomide – binds to cereblon (CRBN) which is a part of the ubiquitin E3 ligase, causes ubiquitinylation of the BRD protein and degradation
Thalidomide

## Slide 40
U937 cells treated with a dilution of mitoxantrone and anthracycline to induce immunogenic cell death
ATP release measured every 10 minutes for 24 hours at 37°C
Comparison of 2D and 3D cell culture model
Notes: JQ1 – thienotriazolodiazepine, potent inhibitor of the BET family of bromodomain proteins (BRD2, BRD3, BRD4 and the testis-specific protein BRDT in mammals)
Thalidomide – binds to cereblon (CRBN) which is a part of the ubiquitin E3 ligase, causes ubiquitinylation of the BRD protein and degradation
Thalidomide

## Slide 41: RealTime-Glo Annexin V Assay
Detects onset of apoptosis by measuring the phosphatidylserin (PS) exposure on surface of the cell membrane
Based on the NanoBiT split NanoLuc luciferase technology
Annexin V conjugated with LgBiT and SmBiT subunits of NanoLuc
Annexin V-LgBiT/SmBiT bind to PS on the membrane → subunits brought to close proximity recombine and restore the NanoLuc luminescent activity
Easily combined with CellTox Green
Notes: Promega vyvinula esej na základě známého markeru apoptózy Annexinu pět, který váže fosfatidylserin. Annexin zfúzovala se dvěma podjednotkami split NanoLuc luciferázy LgBiT a SmBiT. LgBiT a SmBiT k sobě nemají příliš vysokou afinitu. Potřebují nějaký další protein, který by je přivedl k sobě blíž, což se právě stává snadno na vnějším povrchu buňky, která podléhá apoptóze. Buňka vystavuje na svém povrchu fosfatidylserin, na nějž se naváže Annexin, Luciferáza se zkomplementuje a my detekujeme luminiscenci.

## Slide 42: RealTime-Glo Annexin V Assay - Advantages
Different compounds trigger apoptosis with various kinetics in different cell lines
Easily identify the onset of apoptosis caused by your treatment
More information from a single well
Simple no-wash protocol, saves reagents, cells and plates
U2OS cells treated with 1 µM staurosporin at 0 h
Notes: Esej je velmi užitečná buď v případech, ve kterých nevíme přesně, kdy nastává apoptóza a kdy změřit end point esej. Nebo v případech, kdy nás přímo zajímá kinetika apoptózy, protože různé látky způsobují apoptózu s různou kinetikou a to je samo o sobě cenná informace. Díky tomu, že každou jamku měříme mnohokrát opakovaně, tak v porovnání s end point esejí, která by měla získat stejná data, ušetříme obrovské množstí, reagencií, buněk, eseje a tak dále.
A to už je o apoptotických esejích vše. Na tomto místě bych chtěl připomenout, že East Port nedistribuuje jen Promegu.

## Slide 43: CellTox™ Green Cytotoxicity Assay
Penetrated dye significantly enhances its fluorescence
Excluded dye yields very low background fluorescence
Dying cells form pores in the membrane and have compromised membrane integrity
Determines membrane integrity by a non-permeable DNA-binding dye
The dye enters the compromised cells, binds to nuclear DNA and enhances its fluorescence
Notes: Nyní bych se rád zaměřil na kvantifikaci cytotoxicity.
Jak se běžně definuje cytotoxicita? Především jako ztráta integrity cytoplazmatické membrány.
Představím pouze dvě z mnoha esejí pro cytotoxicitu od Promegy. První je CellTox Green, o kterém už byla řeč u CellTiterGlo 3D. Je to barvička, která se váže na DNA, ale není schopná pronikat přes cytoplazmatickou membránu a tudíž se váže jen na DNA v nekrotických buňkách. Tuto vazbu jsme poté schopni detekovat jako vzrůstající zelenou fluorescenci.
Esej má několik výhod.

## Slide 44
CellTox Green Advantages
Dye is nontoxic for at least 72 hodin
= does not affect the IC50 of tested compound (bortezomib)
IC50
72 h CTxG exposure
15 min CTxG exposure
Cell Viability
Well tolerated by the cells
True kinetic assay – measurements for up to 72 hours
Easily multiplex with other fluorescent and BL assays
Suitable for 3D cultures, easily diffuses inside the spheroids
Compatible with standard GFP/FITC filters
Suitable for microplate readers, flow cytometry and fluorescence microscopy
Low price – 1000x dillution for the experiments
Notes: Lze použít pro kinetická měření až po tři dny. Lze zmultiplexovat s luminiscenčními esejemi. Esej je netoxická a buňky lze posléze na cokoliv použít.
Je kompatibilní i s 3D kulturami, jak už jsme viděli dříve. Detekovat lze nejenom v destičkovém readeru, ale i pomocí mikroskopie nebo flow cytometrie pomocí standardních filtrů pro zelenou fluorescenci. A je to esej, která je opravdu levná, takže se vyplatí jí rutinně přidávat do vašich luminiscenčních esejí.

## Slide 45: Flexible Protocol
The reagent can be added:
During cell seeding
With the treatment addition
At the end of the experiment as an end-point assay

## Slide 46
HepG2 cells treated with various doses of terfenadine. Fluorescence measured every hour from the same sample wells.
Live cell kinetic imaging of CellToxTM staining of a paclitaxel treated HepG2 cell spheroid photographed at different times over 2 days. Green fluorescence shows the accumulation of dead cells.
►
Notes: JQ1 – thienotriazolodiazepine, potent inhibitor of the BET family of bromodomain proteins (BRD2, BRD3, BRD4 and the testis-specific protein BRDT in mammals)
Thalidomide – binds to cereblon (CRBN) which is a part of the ubiquitin E3 ligase, causes ubiquitinylation of the BRD protein and degradation
Thalidomide

## Slide 47
Assay Designed for Multiplexing
Can be multiplexed with other kinetic/endpoint assays
Allows differentiation between cytotoxic and cytostatic effect
Allows determining the dose that triggers apoptosis or cytotoxicity

## Slide 48: LDH-Glo® Assay – measures LDH leaking from cells
Lactate dehydrogenase leaks from damaged cells
Its activity is detected in supernatant in a coupled enzymatic reaction
Pro-luciferin is reduced by a proprietary reductase to luciferin and processed by firefly luciferase in the medium
Timed kinetic assay
Suitable for 3D cell cultures
Suitable for measuring antibody-dependent-cell-mediated cytotoxicity (ADCC)
Notes: Další esej pro měření cytotoxicity využívá stejný princip, tedy narušení integrity membrány a kvantifikuje aktivitu laktát dehydrogenázy uniklé z nekrotických buněk. Esejí na měření LDH je na trhu spoustu, ale žádná nedosahuje citlivosti luminiscenční eseje od Promegy.
Esej je založená na detekci NADH, které produkuje LDH oxidací laktátu na pyruvát. NADH je ve spřažené enzymatické reakci použito pro redukci proluciferinu na luciferin. Proluciferin je v tomto typu esejí označován Promegou jako reductase substrate. Luminiscence produkovaná přeměnou tohoto substrátu je přímo úměrná množství LDH.
Esej funguje i pro 3D kultury a je možné ji použít i na měření cytotoxicity typicky u rakovinných buněk, na kterých se zkouší různé nové způsoby biologické léčby. Ať už se jedná buď o monoklonální protilátky, antibody drug conjugates, CAR-T buňky a podobně.

## Slide 49: LDH-Glo® Can be Used as a Kinetic Assay
SKBR3 cells (breast cancer)
Experimental workflow
Enzymatic marker cytotoxicity
Suitable for timed kinetic analysis
For ideal results, use inactivated FBS – higher sensitivity
Notes: Skutečná síla této eseje spočívá v tom, že je možné jí použít v pseudo kinetickém formátu. Tím, že je hodně citlivá, stačí odebrat několik mikrolitrů média v každém časovém bodě, tyto vzorky zamrazit a na konci experimentu všechny naráz změřit. Získáme tak zpětně kinetická data. Příklad takových dat je na grafu vpravo, kde byli buňky rakoviny prsu vystaveny účinku antibody drug konjugátu Kadcyla což je Herceptin-antiHER2 protilátka konjugovaná s mikrotubulárním inhibitorem.

## Slide 50
Different Substrates for Different Purposes
Nano-Glo® Live Cell Assay System
Endpoint / up to 2 h
Nano-Glo® VivazineTM Substrate
2-24 h
Nano-Glo® EndurazineTM Substrate
2 - 72 h
NanoLuc®/NanoBiT® Live Cell Substrates

## Slide 51
Metabolite-selective dehydrogenases coupled to bioluminescent NAD(P)H detection
“With the aid of auxiliary enzymes nearly every substance of biological interest could
be measured with a pyridine nucleotide system”
Oliver Lowry JBC (1961) 236, 2746
Metabolite Assays – One Reaction to Rule Them All
Broad linear range of 3 logs (0,1-100 μM)
Wide dynamic range S/B < 100
High sensitivity, requiring only a small sample volume
Simplified protocol applicable to many sample types – homogenized tissue, 2D & 3D culture, serum, medium
Can be used as timed kinetic assays

## Slide 52
Metabolite-selective dehydrogenases coupled to bioluminescent NAD(P)H detection
Metabolite Assays – One Reaction to Rule Them All
Can be used in a timed kinetic format to measure the signal from supernatant

## Slide 53
Homogenize, then assay
Dillute and assay directly
Homogenize, then assay
Spheroids – direct assay
Metabolite Assays – Compatible Sample Types

## Slide 54
A549; 15,000 cells/well
optionally store
@ -20°C
Glucose and Lactate-Glo Assays
to 50 μl
Only 2–5 μl sample for measurement
Multiple metabolites are easily measured from one sample
Samples can be frozen and measured at the end of the experiment - kinetic information
Investigate glycolysis, a central pathway for providing energy and precursors for biosynthesis
Metabolic profiling of cancer cells, identify vulnerabilities for anti-cancer treatment
Notes: Výhody těchto esejí jsem se rozhodl ukázat na Glucose-Glo a Lactate-Glo. Jsou velmi citlivé, takže stačí pár mikrolitrů média ke stanovení jednoho metabolitu, takže můžeme odebírat vzorky v čase a nebo i pro několik metabolitů naráz. Měřením koncentrace glukózy a laktátu zároveň získáme dobrý globální přehled o metabolizmu buněk, využívání glyklýzy, jako na grafu vpravo nahoře, kde vidíme, jak buňkám během dvou dnů dojde všechna glukóza v médiu a zvyšuje se produkce laktátu.
Zvýšená glykolýza je znakem různých zajímavých buněk, jako rakovinných buněk nebo aktivovaných T-lymfocytů, což je další možné použití eseje.

## Slide 55
GLUTAMATE SECRETION
GLUTAMINE CONSUMPTION
GLUCOSE CONSUMPTION
LACTATE SECRETION
15000
Adapted from Leippe, D et al. (2017), SLAS Discov. 22(4):366-377
7500
2500
55
Multiple Metabolites Offer a More Complete Image
Notes: Ovarian cancer cell lines
OVCAR-3 low invasivness, low glutamine consumption
SKOV-3 high invasiveness, high glutamine consumption

## Slide 56
GLUTAMATE SECRETION
GLUTAMINE CONSUMPTION
OVCAR-3
Moderate glutamine consumption
Low glutamate secretion
Low invasiveness
Adapted from Leippe, D et al. (2017), SLAS Discov. 22(4):366-377
SKOV-3
High glutamine consumption (Glutamine “addicted”)
High glutamate secretion
Highly invasive
56
Multiple Metabolites Offer a More Complete Image

## Slide 57
Glycerol/TAG Assay - Principle
57
Benefits
Quantitative results
No extraction steps, only cell lysis
BL assay = high sensitivity
Simple and fast protocol
Notes: Na základní spřažený systém dehydrogenázy, reduktázy a luciferázy lze napojit i složitější enzymatický systém a detekovat glycerol a triacylglyceroly. Tato esej je zajímavá třeba pro ty, kteří se zabývají jaterními onemocněními. Vzorky se pro tuto esej opět dělí napůl a měří se s a bez přidané lipázy. Ze vzorku bez lipázy zjistíme koncentraci volného glycerolu. Z rozdílu hodnot vzorků s lipázou a bez lipázy zjistíme kolik detekovaného glycerolu ve skutečnosti pocházelo z triglyceridů.
Opět je docela unikátní pro Promegu, že dokáže tyto lipidy kvantifikovat pomocí luminescence bez předchozí extrakce organickými rozpouštědly.

## Slide 58
Glycerol/TAG Assay – Experimental Workflow

## Slide 59: Stimulation and Inhibition of Lipolysis
Isoproterenol
25 nM
3T3L1-MBX fibroblasts plated at 20,000 cells/well and differentiated for 2 weeks to form adipocytes
Insulin
150 nM
+
+
+
-
-
-
Insulin
Isoproterenol
•
Treatment with Isoproterenol and Insulin for 90 min
Notes: Insulin – stimulates absorption of glucose into cells
Isoproterenol – lipolysis inducer

## Slide 60
Quantification of lipogenesis in differentiated 3T3L1-MBX fibroblasts
Lipid content observed at days 5, 12, 14 and 21 of differentiation (A-D respectively)
The cells were either stained with Oil Red O dye or the lipid content was measured by the Glycerol/TAG-Glo assay from Promega
Simple quantification and complementary information to microscopic techniques and flow cytometry

## Slide 61
Cholesterol/Cholesterol Ester Assay
Benefits
Quantitative measurement
No extraction steps, only cell lysis
BL assay = high sensitivity
Simple and quick workflow
Notes: Podobně lze detekovat i cholesterol a cholesterol ester. A tohle je poslední esej, kterou dnes ukazuji. Bylo jich hodně, tak děkuji za trpělivost.

## Slide 62
Cholesterol Assay - Protocol
Measures cholesterol – two measurements have to be done in parallel
  Sample without cholesterol estarase – free cholesterol
  Sample with cholesterol esterase – total cholesterol
Add lytic buffer to the sample (2D or 3D culture, tissue homogenate, serum), incubate at 37 °C
Add detection reagent and incubate for 60 minutes
Detect bioluminescence

## Slide 63
Heating
Shaking
Luminescence
Fluorescence
UV/Vis Absorbance
BRET / FRET
GloMax® Discover
6-, 12-, 24-, 48-, 96- and 384-well
GloMax® Explorer
6-, 12-, 24-, 48-, 96- and 384-well
Heating
Shaking
Luminescence
Fluorescence
Available Upgrades
Vis Absorbance
UV/Vis Absorbance
BRET / FRET
GloMax® Navigator
96-well
Luminescence
Instruments – Features and Configurations
63

## Slide 64: Primary Cells, Stem Cells & Media
Primary cells - over 150 human and animal cell types available
Clonetics media a growth factors for wide spectrum of primary cells
Stem cells together with media
Blood and immune cells from vast collection of donors and sources
  Specialized X-VivoTM media

## Slide 65: Mycoplasma Testing
Mycoplasma = small bacteria lacking cell wall, not susceptible to penicillin and other antibiotics
Widespread contamination in a variety of cell culture systems
Size below 1 μm, hardly visible in optical microscope
BL MycoAlertTM kit:
  Mycoplasma from cell culture supernatant are lysed and their enzymes released into the medium
  Enzymes convert added ADP to ATP
  ATP is processed by firefly luciferase from the detection reagent and in case of contamination bioluminescence is produced

## Slide 66: High Quality Cell Culture Media and Sera
Sera
FBS
Other bovine and animal sera
Human sera
Cell Culture Media
Classic liquid media
Classic powdered media
Special culture media
Cryopreservation
Cell Culture reagents
Supplements and additives
Antibiotics
BSA
Trypsin
Cell separation
Balanced Salt Solutions
Liquid buffers
Powdered buffers
Diagnostics
Virology media
Cytogenetics
German company established in 2013
Specialises on the production of high quality sera and cell culture media and reagents
Possibility of custom manufacturing from 20 liters

## Slide 67
Label-Free Cell Monitoring
Live-cell monitoring of cells in individual culture vessels (Lux microscopes) or 6 to 384 well plates (Omni microscopes)
Compact microscopes placed directly in the incubator
Confluency measurements, scratch assays, colony counting
Fluorescence versions – fluorescent object counting
Notes: Další náš dodavatel, který je relevantní pro dnešní přednášku o buněčných esejích je Cytosmart. Nabízí různě velké a různě komplexní mikroskopy pro live cell imaging přímo v inkubátoru. Pomocí těchto mikroskopů můžete například sledovat jak se během několik dní mění konfluence buněk, což je další způsob testování viability nebo cytotoxicity.
Můžeme vám snadno zařídit demo těchto přístrojů nebo vás propojit se zákazníky tady v Česku, kteří už Cytosmart mikroskopy používají.
Úplně na závěr bych vás chtěl upozornit na další zdroj informací.

## Slide 68: Thank you for your attention!
Questions?